## Slide 1
PV 204 SECURITY TECHNOLOGIES
Term Project: Phase 1 Security Certificate Analysis
SMARTY IQ-GPRS / LTE, VERSION 1.0
UCO 502606
Amal Chukkinin
FI, MUNI

## Slide 2: Basics of device certified (ToE).
  Target of Evaluation (TOE) is called:
-SMARTY IQ-GPRS / LTE, Version 1.0
-Electronic unit comprising hardware, software and firmware.

## Slide 3: Certified by
SMARTY IQ-GPRS / LTE, Version 1.0 has undergone the certification procedure at BSI.
The evaluation of the product SMARTY IQ-GPRS / LTE, Version 1.0 was conducted by TÜV Informationstechnik GmbH which is an evaluation facility (ITSEF)6 recognised by the certification body of BSI.
The product was developed by: Sagemcom Dr. Neuhaus GmbH.

## Slide 4: Attacker Model Discussed
Local Attacker:- Attackers having physical access to Meter, Gateway, a connection between these components, or local logical access to any of the interfaces, trying to disclose or alter assets while stored in the Gateway.
WAN attacker:- An attacker located in the WAN trying to compromise the confidentiality and or integrity of the processed Meter Data and or configuration data transmitted via the WAN
Successful attack of a local attacker will always only impact one Gateway.

## Slide 5: The attacker may violate/modify:-
Modify (i.e. alter, delete, insert, replay or redirect) Meter Data when transmitted between Meter and Gateway, Gateway and consumer, or Gateway and external entities.
Attacker may try to alter the Gateway time.
A WAN attacker may try to violate the privacy of the consumer by disclosing Meter Data or configuration data.
A WAN or local attacker may try to access (i.e. read, alter, delete) information to which they don't have permission to while the information is stored in the TOE.

## Slide 6: Device VS Attacks
The security objectives are:-
  Firewall.
  Separate IF.
  Conceal.
  Meter.
  Cryptographic Functions.
  Time.
  Protection against malfunction and tampering.
  Management.
  Access.

## Slide 7: Countering the Threats
Data Modification by Local Attacker -O.Meter, O.Crypt and PhysicalProtection
Data Modification WAN Attacker -O.Firewall and O.Crypt.
TimeModification- O.Time, O.Crypt and PhysicalProtection.
Privacy-O.Meter, O.Crypt and O.Firewall.
Infrastructure - O.Firewall, O.SeparateIF, O.Meter and O.Crypt

## Slide 8: Security Assurance Requirements (SARs)
Assurance Class:- Development
Assurance Component:-
  ADV_ARC.1 , ADV_FSP.4 , ADV_IMP.1
Assurance Class:- Guidance Documents
Assurance Component:-
* AGD_OPE.1,AGD_PRE.1
Assurance Class:- Life Cycle Support
Assurance Component:-
  ALC_CMC.4, ALC_CMS.4, ALC_TAT.1

## Slide 9
Assurance Class:- Security Target evaluation
Assurance Component:-
  ASE_CCL.1, ASE_ECD.1
Assurance Class:- Tests
Assurance Component:-
ATE_COV.2 , ATE_DPT.1
Assurance Class:- Vulnerability Assessment
Assurance Component:-
  AVA_VAN.3

## Slide 10: Security Functional Requirements (SFRs)
(a) Security Audit
(b) Communication:- Enforced proof of origin
(c)Cryptographic Support
(d) User Data Protection
(e) Identification and Authentication
(f) Security Management
(g) Privacy
(h) Trusted Path or channels

## Slide 11: What is Out of Scope?
Indeed this Security Target acknowledges that the Gateway and the Meters have no possibility at all to impact the delivery of a commodity. Even an intentional stop of the delivery of a certain commodity is not within the scope of this Protection Profile.
Exact regulations regarding the Processing Profiles and the Gateway Administrator are beyond the scope of this Security Target.
Whether a deviation between the time source(s) in the WAN and the local system time is still acceptable, normative or legislative regulations shall be considered.
It should be noted that depending on the kind of application a more accurate system time is needed. But this aspect is not within the scope of this Protection Profile.

## Slide 12: Conclusion and Evaluation
All components of the EAL 4 package including the class ASE as defined in the CC.
The components AVA_VAN.5 and ALC_FLR.2 augmented for this TOE evaluation.
The evaluation has confirmed assurance, functionality and conformance.
Cryptographic functionalities used efficiently inside the TOE to enforce the security policy and outlines the standard of application.
Limited validity for the usage of cryptographic algorithms as outlined and has to be considered by the user and his system risk management process.
Overall the evaluation by the lab is excellent and the certificate is having a validity of 8 years combined with regular mandatory re- assessment after every 2 years.

## Slide 13
Thank You!